## Slide 1: Renewable Energy Pathways to Support Carbon Neutrality in China
William Gao

## Slide 2: To achieve carbon neutrality in China, how much renewable resources should be built? Where, and when?

## Slide 3: Outline
Optimization model for power system planning at large
Original paper: China’s renewable energy pathways toward carbon neutrality
Decadal snapshot model

## Slide 4: Optimization Models for power system planning at large

## Slide 5: Optimization Methods
Given constraints and an objective, how should we tune the variables of interest (decision variables) such that the objective is maximized (or minimized)?
Example: Factory production. A factory wants to produce two types of widgets, A and B, to maximize its profit.
  Widget A generates $150 revenue per widget
  Widget B generates $175 revenue per widget
  Producing one unit of A requires 7 units of material M
  Producing one unit of B requires 11 units of material M
  The supply of M is limited to 77 units in total
Credit: Power System Optimization , Davidson & Jenkins

## Slide 7: Why use optimization models on power system planning?
Optimization is widely used in operations of power system (e.g. electricity dispatch), but here I am focusing on planning alone
Increasingly, pressure from climate change and emission targets – system-level planning is critical
Provide a concrete scaffold for policymakers
Anticipate potential constraints and challenges

## Slide 8: Original paper: China’s renewable energy pathways toward carbon neutrality

## Slide 10: At the year 2060, how much renewable energy resources, transmission capacity, and energy storage should China have to meet the carbon neutrality goal?

## Slide 12: Firm power as exogenous parameters
Taking firm power as exogenous parameters/inputs
  250 GW Combined Heat and Power (CHP) with carbon capture and sequestration (CCS) [heating]
  110 GW of Bioenergy with CCS (BECCS) [negative sink]
  218 GW nuclear
  580 GW hydro
  320 GW natural gas with CCS (NGCCS)

## Slide 13: Decision variables: renewable, transmission, storage
Tuning for decision variables:
  Wind
    on-shore
    off-shore
  Solar PV
  Supporting infrastructures
    Transmission
      Inter-provincial high voltage transmission line capacity
      Intra-provincial spur and trunk lines
    Energy storage
      Pumped hydro storage (PHS), utility-scale batteries

## Slide 14: Model feature 1: spatially-explicit RE resources
Renewable energy buildouts at a grid cell level
  Spatial resolution: 0.3125° lon x 0.25° lat
  Wind energy potential
  Utility-scale solar energy potential
  Distributed solar PV
  Land suitability
    Slope
    Land type + suitability factor

## Slide 16: Model feature 2: Provincial focus
Supply-demand balance maintained at a provincial level
Allowing inter-regional transmission through high-voltage transmission line

## Slide 17: Decadal Snapshots Adaptation

## Slide 19: Core Ideas
Run model four times sequentially at 2030, 2040, 2050, and 2060.
At the snapshot years, the outputs (brownfield capacity build) will be used as the inputs for the next model.
Hold exogenous fixed parameters constant for each model across all years.
Project time varying parameters into the future, before feeding them into models as inputs.

## Slide 20: Exogenous Fixed Parameters
VRE maximum potentials
Location of load center and substations
Life spans
Firm power parameters
  Ramp up & down cost
  Ramp up & down rate
  Reserve cost
  Max generation capacity
  Capacity factor (for hydro)
  Min generation
Firm power with CCS parameters
  Power loss
  CO2 capture rate
Energy storage parameters
  Pump hydro capacity
  Charge & discharge efficiency
  Round trip efficiency
  Self-discharge rate
VRE parameters
  Hourly capacity factor
Reserve requirement
  Firm generation
  VRE generation
Transmission line parameters
  Power loss rate
VRE potentials, locations, energy specific specifications

## Slide 21: Time-Varying Parameters
Hourly electricity demand
Cost of non-VRE generation resources
  CapEx
  Fuel cost
  O&M cost
Cost of VRE generation resources
  LCOE
Cost of batteries
  CapEx
  O&M cost
Cost of transmission lines
  CapEx
Electricity demand, O&M cost, fuel cost, CapEx, firm power capacity
Firm power capacity
  Coal, Coal CHP, Coal CHP CCS
  Gas, Gas CCS
  BECCS
  Nuclear
  Hydro

## Slide 22: Brownfield Capacity Build
Gridded Solar generation capacity
  Distributed solar
  Utility-scale solar
Gridded Wind generation capacity
  Onshore
  Offshore
Transmission capacity
  Trunk & spur line
  Inter-provincial
Storage capacity
RE Generation capacity, storage capacity, transmission capacity

## Slide 23: Challenge: unabated firm power phaseout, especially coal

## Slide 24: Specifically…
The 2060 model assumes exogenous firm power capacity, and all unabated coal and gas are phased out by 2060.
But China now has over 10,000 GW of total coal generation capacity.
For the decadal snapshots, how should we adjust firm power capacity?

## Slide 25: Emission-guided early retirement approach (for coal)
Core idea: bounded by an emission trajectory for the power sector, decide which coal plants should enter early retirement after accounting for natural retirement.
Data: Global Energy Monitor – Coal plants tracker
Assumptions:
  All permitted power plants will be built
  All plants under construction will be operational
  Planned lifetime of a power plant is between 20 to 30 years
  Except for mentioned plants, no new coal plants will be built.

## Slide 26: Natural Retirement

## Slide 27: Some wrinkles… data availability
Some retired plants has operation start year but no retirement year
  Use operation start year to predict the lifetime of retired plants (

## Slide 28: Early Retirement
Created combined retirement score
Consider three aspects when deciding which plants should retire first
  Technical attributes
  Profitability
  Environmental impacts
Score for each GEM plants

## Slide 29: Evaluation details
Credits: Cui et al.

## Slide 30: Putting everything together
emission gap = projected emission in power sector – reduction in emission from coal plants natural retirement
Decide early retirement: keep retiring plants with the lowest combined retirement score, until the sum of emission reduction from early retirement covers the emission gap

## Slide 31: Thank you! What are your questions and feedbacks?